Ion dynamics in the H-1 Helical Axis Stellarator

Experimental/computational

John Howard

Research School of Physical Sciences and Engineering

john.howard@anu.edu.au

wwwrsphysse.anu.edu.au/~jnh112/AIIM/index.htm

Objective

To better understand the mechanisms leading to ion heating in the H-1 heliac.

Description

The H-1 heliac Major National Research Facility in the Research School of Physical Sciences at the Australian National University is a toroidal magnetic confinement device for the study of high-temperature fusion-relevant plasma physics.

H-1 is equipped with a number of high-power (>100kW) systems for heating electrons and ions to temperatures of the order of 106 K by resonantly exciting them at their cyclotron frequency and harmonics.  This produces a population of energetic particles which then thermalize with the background plasma.

We have recently developed novel “time-domain” imaging systems that for the first time allow two-dimensional high-speed imaging of plasma ion temperature and flows based on the Doppler broadening and shifting of spectral emission lines.  These capabilities allow detailed study of the resonant absorption processes that heat ions, as well as ion energy transport processes.  The system also allows direct imaging of plasma flow fields which can vary in response to the changing ion temperature.

The project would involve the use of power modulation methods and development of suitable signal processing techniques to allow extended velocity-space imaging of the ion velocity distribution function and its evolution.

References

See:  http://wwwrsphysse.anu.edu.au/~jnh112/AIIM/Coherence_imaging.htm